## Slide 1: Data Center Networking
K. K. Ramakrishnan
UCR
(most of the slides – thanks to Prof. Dan Li, Tsinghua University, Beijing, China. A few from the textbook, and a couple from slides from V. Arun, Umass Amherst.

## Slide 2: Cloud is built on Massive Datacenters
Range in size from “edge” facilities to megascale (100K to 1M servers)
Economies of scale
  Approximate costs for a small size center (1K servers) and a larger, 400K server center.
This data center is
11.5 times
the size of a football field
Technology | Cost in small-sized Data Center | Cost in Large Data Center | Ratio
Network | $95 per Mbps/ Month | $13 per Mbps/ month | 7.1
Storage | $2.20 per GB/ Month | $0.40 per GB/ month | 5.7
Administra-tion | ~140 servers/ Administrator | >1000 Servers/ Administrator | 7.1
(Courtesy of Dennis Gannon, 2010)

## Slide 3: Data Centers
Data
Centers
Cloud
Computing
Collaboration
SLA Metrics
Empowered User
Global Availability
Reg. Compliance
Power & Cooling
Provisioning
Asset Utilization
Security Threats
Bus. Continuance
Notes: While cloud computing is considered as a logical concept, it is in fact constructed by data centers.
A data center is a facility used to house computer systems and associated components, such as telecommunications and storage systems. It generally includes redundant or backup power supplies, redundant data communications connections, environmental controls (e.g., air conditioning, fire suppression) and security devices.

## Slide 4: What are data centers?
Data centers are an aggregation of compute, memory, and storage resources.

## Slide 5: What is a server?
A server is a computing machine under a predefined form factor.
A server consists of
  One or several power-hungry multi-core processors
  Multiple GPU/FPGA/ASIC accelerators
  Massive memory capacity
  High-bandwidth networking bandwidth
  Enormous persistent HDD/SSD storage

## Slide 6: What are data center networks?
Data center networks connect servers

## Slide 7: Data center networks
10’s to 1000’s of thousands of hosts/servers, often closely coupled, in close proximity:
  e-business (e.g. Amazon – 28 data centers, 1.5 M servers, 2014)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google – estimate had 2.5M servers in 2016)
challenges:
  multiple applications, each serving massive numbers of clients
  managing/balancing load, avoiding processing, networking, data bottlenecks
Inside a 40-ft Microsoft container,
Chicago data center

## Slide 8: How do data center networks connect servers?
Data center networks connect servers via NIC ports!
Management port:
  Configure and manage a baseboard management controller (BMC)
Management

## Slide 9: How do data center networks connect servers?
Data center networks connect servers via NIC ports!
Control network port:
  Load the server OS and set up the network
  Initiate and upgrade the server configurations
Control

## Slide 10: How do data center networks connect servers?
Data center networks connect servers via NIC ports!
Data network port:
  Carry application traffic
Data

## Slide 11: Data center networks provide connectivity for all three ports
BMC: an ARM-based SoC with graphics and control logic built-in
  Vendor: ASPEED
  There are non-ARM solutions
Type #1: Management Traffic

## Slide 12: Data center networks provide connectivity for all three ports
Target user: server administrator
  No need to enter the server room physically to perform tasks
Type #1: Management Traffic
Management traffic characteristics:
  Reliable connectivity between server BMC and admin host
  Low traffic volume
  Low performance requirement
  No server-server communication

## Slide 13: Data center networks provide connectivity for all three ports
An out-of-band network for server configuration and maintenance
  A 1G/10G/25G onboard integrated NIC or external one
  OS load/upgrade, system setup, health monitoring, SSH, ...
Target user: server user or infrastructure engineer
  Responsible for refactoring servers in a way that satisfies applications
  Becoming increasingly important today
Type #2: Control Traffic

## Slide 14: Data center networks provide connectivity for all three ports
An out-of-band network for server configuration and maintenance
  A 1G/10G/25G onboard integrated NIC or external one
  OS load/upgrade, system setup, health monitoring, SSH, ...
Target user: server user or infrastructure engineer
  Responsible for refactoring servers in a way that satisfies applications
  Becoming increasingly important today
Type #2: Control Traffic
Control traffic characteristics:
  Reliable connectivity control port and control host
  Modest traffic volume
  Modest performance requrirement
  Partial server-server communication

## Slide 15: Data center networks provide connectivity for all three ports
An in-band network for data center applications
  Dominated by external PCIe-based NICs
  Vendor: NVIDIA/Mellanox, Broadcom, Intel, ...
Target user: application developers
  Bandwidth keeps increasing: 1G->10G->25/40G->100G->200G->400G
  More data ports are added for different use cases.
Type #3: Data Traffic

## Slide 16: Data center networks provide connectivity for all three ports
An in-band network for data center applications
  Dominated by external PCIe-based NICs
  Vendor: NVIDIA/Mellanox, Broadcom, Intel, ...
Target user: application developers
  Bandwidth keeps increasing: 1G->10G->25/40G->100G->200G->400G
  More data ports are added for different use cases.
Type #3: Data Traffic
Data traffic characteristics:
  Reliable connectivity among servers
  High traffic volume
  High performance requirement

## Slide 17
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
Load
balancer
Load
balancer
B
1
2
3
4
5
6
7
8
A
C
Border router
Access router
Internet
Data center networks
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)

## Slide 18
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
1
2
3
4
5
6
7
8
Data center networks
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy

## Slide 19: Broad questions
How are massive numbers of commodity machines networked inside a data center?
Virtualization: How to effectively manage physical machine resources across client virtual machines?
Operational costs:
  Server equipment
  Power and cooling
  Networking

## Slide 20
Source: NRDC research paper

## Slide 21: Breakdown wrt DC size
Source: NRDC research paper

## Slide 22: Data Center Costs
Total cost varies
  upwards of $1/4 B for mega data center
  server costs dominate
  network costs is still significant
Long provisioning timescales:
  new servers purchased quarterly at best
Amortized Cost* | Component | Sub-Components
~45% | Servers | CPU, memory, disk
~25% | Power infrastructure | UPS, cooling, power distribution
~15% | Power draw | Electrical utility costs
~15% | Network | Switches, links, transit
  *3 yr amortization for servers, 15 yr for infrastructure; 5% cost of money

## Slide 23
Table 2: Economies of Scale in 2006 for medium-sized datacenter (1000 servers) vs. very large datacenter (50,000 servers). [24]
(Courtesy of M. Ambrust, et al 2009)

## Slide 24
Cost Considerations : Power, Cooling, Physical Plant, and Operational Costs
(Courtesy of M. Ambrust, et al 2009)

## Slide 25: DC network design questions
Core and aggregation switches much faster than ToR switches
How much faster should core and aggregation switches need to be than ToR switches?
How many ports do core/aggregation switches need to support for a given number of ToR switch ports?
How many cables need to be run in total for a N machine datacenter?
What bisection bandwidth can be achieved?
Q: Why can’t we just build a single BIG switch to interconnect all machines?

## Slide 26: Data Center Design Requirements
Data centers typically run two types of applications
  outward facing (e.g., serving web pages to users)
  internal computations (e.g., MapReduce for web indexing)
Workloads are often unpredictable:
  Multiple services run concurrently within a DC
  Demand for new services may spike unexpectedly
    Spike of demands for new services mean success!
    But this is when success spells trouble (if one is not prepared)!
Failures of servers are the norm
  Recall that GFS, MapReduce, etc., resort to dynamic re-assignment of chunkservers, jobs/tasks (worker servers) to deal with failures; data is often replicated across racks, …
  “Traffic matrix” between servers are constantly changing

## Slide 27: Data Center Costs
Total cost varies
  upwards of $1/4 B for mega data center
  server costs dominate
  network costs significant
Long provisioning timescales:
  new servers purchased quarterly at best
Amortized Cost* | Component | Sub-Components
~45% | Servers | CPU, memory, disk
~25% | Power infrastructure | UPS, cooling, power distribution
~15% | Power draw | Electrical utility costs
~15% | Network | Switches, links, transit
  *3 yr amortization for servers, 15 yr for infrastructure; 5% cost of money

## Slide 28: Networking Objectives
Provide Uniform high capacity
  Capacity between servers limited only by their NICs
  No need to consider topology when adding servers
    => In other words, high capacity between any two servers no matter which racks they are located in!
Have Performance isolation
  Traffic of one service should be unaffected by others
Ease of management: “Plug-&-Play” (layer-2 semantics)
  Flat addressing, so any server can have any IP address
  Server configuration is the same as in a LAN
  Legacy applications depending on broadcast must work

## Slide 29: Cisco Recommended DC Structure: (Early days)
Internet
CR
CR
AR
AR
AR
AR
…
S
S
LB
LB
Data Center
Layer 3
Internet
S
S
A
A
A
…
S
S
A
A
A
…
…
Layer 2
Key:
CR = L3 Core Router
AR = L3 Access Router
S = L2 Switch
LB = Load Balancer
A = Rack of 20 servers
with Top of Rack switch

## Slide 30: A Scalable, Commodity Data Center Network Architecture
Main Goal: addressing the limitations of today’s data center network architecture
  single point of failure
  Over-subscription of links higher up in the topology
Key Design Considerations/Goals
  Allows host-host communication at line speed
    no matter where they are located!
  Backwards compatible with existing infrastructure
    no changes in application & support of layer 2 (Ethernet)
  Cost effective
    cheap infrastructure
    and low power consumption & heat emission

## Slide 31
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
1
2
3
4
5
6
7
8
Data center networks: Fat Tree
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy

## Slide 32: Fat-Tree Based Topology (Cont.)
Why Fat-Tree?
  Fat tree has identical bandwidth at any bisection
    Bisection bandwidth: bandwidth across smallest cut that divides network into two equal halves
    Bandwidth across “narrowest” part of the network
  Each layer has the same aggregated bandwidth
Can be built using cheap devices with uniform capacity
  Each port supports same speed as end host
  All devices can transmit at line speed if packets are distributed uniformly along available paths
Great scalability
  k-port switch supports k3/4 servers

## Slide 33: Fat-Tree Based Topology (Cont.)
Why Fat-Tree?
  Fat tree has identical bandwidth at any bisection
    Bisection bandwidth: bandwidth across smallest cut that divides network into two equal halves --- Bandwidth across “narrowest” part of the network
  Each layer has the same aggregated bandwidth

## Slide 34: Bisection Bandwidth in a Fat Tree

## Slide 35: Fat-Tree Based Topology (Cont.)
Why Fat-Tree?
  Fat tree has identical bandwidth at any bisection
    Bisection bandwidth: bandwidth across smallest cut that divides network into two equal halves
    Bandwidth across “narrowest” part of the network
  Each layer has the same aggregated bandwidth
Can be built using cheap devices with uniform capacity
  Each port supports same speed as end host
  All devices can transmit at line speed if packets are distributed uniformly along available paths
Great scalability
  k-port switch supports k3/4 servers

## Slide 36: Outline
Data Center Introduction
Data Center Network Architectures
Fat-Tree
VL2
DCell
BCube
FiConn

## Slide 37: Data Center Networking
Major Theme:
What are new networking issues posed by large-scale data centers?
Network Architecture
Topology design
Addressing
Routing
Forwarding

## Slide 38: Data Center Interconnection Structure
Nodes in the system: racks of servers
How are the nodes (racks) inter-connected?
  Typically a hierarchical inter-connection structure
Original, typical smallish-data center structure
  starting from the bottom level
  rack switches
  1-2 layers of (layer-2) aggregation switches
  access routers
  core routers
Is such an architecture good enough?

## Slide 39: Design Characteristics of a Data Center Network
Topology (how things are connected):
  Crossbar, ring, 2-D and 3-D meshes or torus, hypercube, tree, butterfly, perfect shuffle ....
Routing algorithm (path used):
  Example in 2D torus: all east-west then all north-south (avoids deadlock).
Switching strategy:
  Circuit switching: full path reserved for entire message, like the telephone network
  Packet switching: message broken into separately-switched/routed packets.
Flow control (what if there is congestion):
  Stall, store data temporarily in buffers, re-route data to other nodes, tell source node to temporarily halt, discard, etc.

## Slide 40: Performance Properties of a Network: Bisection Bandwidth
Bisection bandwidth: bandwidth across smallest cut that divides network into two equal halves
Bandwidth across “narrowest” part of the network
bisection
cut
not a
bisection
cut
bisection bw= link bw
bisection bw = sqrt(n) * link bw
Bisection bandwidth is important for algorithms in which all processors need to communicate with all others

## Slide 41: Cisco Recommended DC Structure: Illustration
Internet
CR
CR
AR
AR
AR
AR
…
S
S
LB
LB
Data Center
Layer 3
Internet
S
S
A
A
A
…
S
S
A
A
A
…
…
Layer 2
Key:
CR = L3 Core Router
AR = L3 Access Router
S = L2 Switch
LB = Load Balancer
A = Rack of 20 servers
with Top of Rack switch

## Slide 42: Data Center Design Requirements
Data centers typically run two types of applications
  outward facing (e.g., serving web pages to users)
  internal computations (e.g., MapReduce for web indexing)
Workloads often unpredictable:
  Multiple services run concurrently within a DC
  Demand for new services may spike unexpectedly
    Success: spike of demands for new services!
    But this is when success spells trouble (if one is not prepared)!
Failures of servers are the norm
  Recall that GFS, MapReduce, etc., resort to dynamic re-assignment of chunkservers, jobs/tasks (worker servers) to deal with failures; data is often replicated across racks, …
  “Traffic matrix” between servers are constantly changing

## Slide 43: Overall Data Center Design Goals
Important Goals
Agility – Any service, Any Server
Turn the servers into a single large fungible pool
  Let services “breathe”: dynamically expand and contract their footprint as needed
    We see this is done for Google’s GFS, BigTable, MapReduce
Increase service developer productivity
Lower cost
Achieve high performance and reliability
These are the motivators for most data center infrastructure projects!

## Slide 44: Achieving Agility …
Workload Management
  means for rapidly installing a service’s code on a server
  dynamic cluster scheduling and server assignment 
    E.g., MapReduce, Bigtable, …
  virtual machines, disk images 
Storage Management
  means for a server to access persistent data
  distributed file systems (e.g., GFS) 
Network Management
  Means for communicating with other servers, regardless of where they are in the data center
  Achieve high performance and reliability

## Slide 45: Networking Objectives
Uniform high capacity
  Capacity between servers limited only by their NICs
  Should not have to consider network topology when adding servers
    => In other words, high capacity between any two servers no matter which racks they are located in!
Performance isolation
  Traffic of one service should be unaffected by others
Ease of management: “Plug-&-Play” (layer-2 semantics)
  Flat addressing, so any server can have any IP address
  Server configuration is the same as in a LAN
  Legacy applications depending on broadcast must work

## Slide 46: Additional Data Center Considerations
Internet
CR
CR
AR
AR
AR
AR
…
S
S
LB
LB
Data Center
Layer 3
Internet
S
S
A
A
A
…
S
S
A
A
A
…
…
Layer 2
Key:
CR = L3 Core Router
AR = L3 Access Router
S = L2 Switch
LB = Load Balancer
A = Top of Rack switch
Uniform high capacity?
Performance isolation?
typically via VLANs
Agility in terms of dynamically adding or shrinking servers?
Agility in terms of adapting to failures, and to traffic dynamics?
Ease of management?
Hierarchical network; 1+1 redundancy
Equipment higher in the hierarchy handles more traffic
  more expensive, more effort for availability  scale-up design
Servers connect via 1-10 Gbps UTP to Top-of-Rack switches
Other links are mix of 1G, 10G, 100G; fiber, copper

## Slide 47: Modern Data Center Network Architectures: Options
Switch-centric
  Servers use only 1 port for connection
  Interconnection and routing intelligence put into switches
  Fat-Tree, PortLand, VL2
Server-centric
  Servers use multiple ports
  Participate in packet forwarding
  DCell, FiConn, BCube, MDCube, CamCube

## Slide 48: Outline
Data Center Introduction
Data Center Network Architectures
Fat-Tree
VL2
DCell
BCube
FiConn

## Slide 49: A Scalable, Commodity Data Center Network Architecture
Main Goal: addressing the limitations of today’s data center network architecture
  single point of failure
  Over-subscription of links higher up in the topology
Key Design Considerations/Goals
  Allows host-host communication at line speed
    no matter where they are located!
  Backwards compatible with existing infrastructure
    no changes in application & support of layer 2 (Ethernet)
  Cost effective
    cheap infrastructure
    and low power consumption & heat emission

## Slide 50: Fat-Tree Based DC Architecture
Inter-connect racks (of servers) using a fat-tree topology
Fat-Tree: a special type of Clos Network (after C. Clos)
  K-ary fat tree: three-layer topology (edge, aggregation and core)
  each pod consists of (k/2)2 servers & 2 layers of k/2 k-port switches
  each edge switch connects to k/2 servers & k/2 aggr. switches
  each aggr. switch connects to k/2 edge & k/2 core switches
  (k/2)2 core switches: each connects to k pods; (Total: k3/4 servers)
Using 2-level routing table, pkts. from source 10.0.1.2 to 10.2.0.3 take the dashed path
Fat-tree
with K=4
[UCSD] A Scalable Commodity Data Center Network Architecture:
M. Al-Fares, A. Loukissas, A. Vahdat. ACM SIGCOMM 2008, pages 63-74.

## Slide 51: Fat tree topology
Core branches, i.e., those near the top of the hierarchy, are fatter or higher in capacity
e.g., 48- port GigE switches; consist of 48 pods, edge layer + aggregation layer w/24 switches each. Edge switches in every pod assigned to 24 hosts each.

## Slide 52: Bisection of Fat Tree
Architecture provides full bisection bandwidth and
there is no oversubscription at the aggregation and edge switches.

## Slide 53: Why simpler hierarchies not good enough?
High cost
High oversubscription (ratio of worst-case aggregate bandwidth among end-hosts to bisection bandwidth)

## Slide 54: Fat-tree Topology is Great, But …
Is using fat-tree topology to inter-connect racks of servers by itself sufficient?
What routing protocols should we run on these switches?
Layer 2 switch algorithm: results in data plane flooding!
Layer 3 IP routing:
  shortest path IP routing will typically use only one path despite the path diversity in the topology
  if using equal-cost multi-path routing at each switch independently and blindly, packet re-ordering may occur; further load may not necessarily be well-balanced
  And: control plane flooding!

## Slide 55: Optimizations to Distribute traffic
Flow classification
  Eliminates local congestion
  Assign traffic to ports on a per-flow basis instead of a per-host basis
Flow scheduling
  Eliminate global congestion
  Prevent long lived flows from sharing the same links
    Assign long lived flows to different links

## Slide 56: Design Goals for Network Fabric
Main consideration: Support for Agility
Easy configuration and management: plug-&-play
Fault tolerance, routing and addressing: scalability
Commodity switch hardware: small switch state
Virtualization support: seamless VM migration
Useful to evaluate approaches: Layer-2 (Ethernet w/ flat-addressing) vs. layer-3 (IP w/ prefix-based addressing) based on these considerations:
  plug-&-play?
  scalability?
  small switch state?
  seamless VM migration?

## Slide 57: FAT-Tree Modified
Enforce a special (IP?) addressing scheme in DC
  Unused.PodNumber.switchnumber.Endhost
  Allows hosts attached to same switch to route only through switch
  Allows intra-pod traffic to stay within pod
Use two level look-ups to distribute traffic and maintain packet ordering
First level is prefix lookup
  used to route down the topology to servers
Second level is a suffix lookup
  used to route up towards core
  maintain packet ordering by using same ports for same server

## Slide 58: Fat Tree Routing Example
Send packet from 10.0.1.2 to 10.2.0.3

## Slide 59: Fat Tree Routing Example
At Switch (10.0.2.1)
dest ip = 10.2.0.3
since no prefix exists, follow default and go to suffix table
Suffix = 3 ( from dest IP 10.2.0.3)
Output port =3 to 10.4.1.2
Prefixes | Port
10.0.0.0/24 | 0
10.0.1.0/24 | 1
0.0.0.0/8 | 
S: 10.0.2.1
Sufffixes | Port
0.0.0.2/8 | 2
0.0.0.3/8 | 3
0
1
2
3
0
1
2
3

## Slide 60: Fat Tree Routing Example
At Switch (10.4.1.2)
dest ip = 10.2.0.3
prefix exists
Output port =2 to 10.2.2.1
Prefixes | Port
10.0.0.0/16 | 0
10.1.0.0/16 | 1
10.2.0.0/16 | 2
10.3.0.0/16 | 3
S: 10.4.1.2
0
1
2
3

## Slide 61: Fat Tree Routing Example
At Switch (10.2.2.1)
dest ip = 10.2.0.3
Terminating prefix exists
  (i.e. destination host on current pod)
Output port = 0 to 10.2.0.1
Prefixes | Port
10.2.0.1/24 | 0
10.2.1.0/24 | 1
0.0.0.0/8 | 
S: 10.2.2.1
Prefixes | Port
0.0.0.2/8 | 3
0.0.0.3/8 | 2
0
1
2

## Slide 62: Fat Tree Routing Example
At Switch (10.2.0.1)
dest ip = 10.2.0.3
Terminating switch
Standard switching techniques deliver packet to end host
Prefixes | Port
10.2.0.0/24 | 0
10.2.1.0/24 | 1
0.0.0.0/8 | 
S: 10.2.0.1
Prefixes | Port
0.0.0.2/8 | 3
0.0.0.3/8 | 2

## Slide 63: Fat Tree Routing Example All tables
Prefixes | Port
10.0.0.0/24 | 0
10.0.1.0/24 | 1
0.0.0.0/8 | 
S: 10.0.1.1
Prefixes | Port
0.0.0.2/8 | 3
0.0.0.3/8 | 2
Prefixes | Port
10.0.0.0/24 | 0
10.0.1.0/24 | 1
0.0.0.0/8 | 
S: 10.0.2.1
Prefixes | Port
0.0.0.2/8 | 2
0.0.0.3/8 | 3
Prefixes | Port
10.0.0.0/16 | 0
10.1.0.0/16 | 1
10.2.0.0/16 | 2
10.3.0.0/16 | 3
S: 10.4.1.2
Prefixes | Port
10.2.0.1/24 | 0
10.2.1.0/24 | 1
0.0.0.0/8 | 
S: 10.2.2.1
Prefixes | Port
0.0.0.2/8 | 3
0.0.0.3/8 | 2
Prefixes | Port
10.2.0.0/24 | 0
10.2.1.0/24 | 1
0.0.0.0/8 | 
S: 10.2.0.1
Prefixes | Port
0.0.0.2/8 | 3
0.0.0.3/8 | 2

## Slide 64: PortLand: A Scalable Fault-Tolerant Layer 2 Data Center Network Fabric
PortLand is a single “logical layer 2” data center network fabric that is meant to enable large scale
PortLand internally separates host identity from host location
  Uses IP address as host identifier
  introduces “Pseudo MAC” (PMAC) addresses internally to encode endpoint location
PortLand runs on commodity switch hardware with unmodified hosts
Read: Sigcomm 2009 paper on Portland, from UCSD

## Slide 65: PortLand Solution
Assume: a Fat-tree network topology for DC
Introduce “pseudo MAC addresses” to balance the pros and cons of flat- vs. topology-dependent addressing
PMACs are “topology-dependent,” hierarchical addresses
  But used only as “host locators,” not “host identities”
IP addresses used as “host identities” (for compatibility w/ apps)
Pros: small switch state & Seamless VM migration
Pros: “eliminate” flooding in both data & control planes
But requires a IP-to-PMAC mapping and name resolution
  a location directory service
And location discovery protocol & fabric manager
  for support of “plug-&-play”

## Slide 66: PMAC Addressing Scheme
PMAC (48 bits): pod.position.port.vmid
  Pod: first 16 bits; position and port (8 bits each); vmid: last 16 bits
Assign only to servers (end-hosts) – by switches
2
3
0
1
2
3
Core
Aggregation
Edge
Pod
Position
Port

## Slide 67: Location Discovery Protocol
Location Discovery Messages (LDMs) exchanged between neighboring switches
Switches self-discover location on boot up
  Location Characteristics Technique
  Tree-level (edge, aggr. , core) auto-discovery via neighbor connectivity
  Position # aggregation switch help edge switches decide
  Pod # request (by pos. 0 switch only) to fabric manager
Aggregation
Edge
Core
0
1
0
1
1
0
2
3
0
1

## Slide 68: PortLand: Name Resolution
Edge switch listens to end hosts, and discover new source hardware MACs and IP address based on ARP source info’
Edge switch can assign the Pseudo MAC address for each host-VM (it knows the pod#, position. has to assign a Vmid)
Installs <IP, PMAC> mappings for the source of the ARP, and informs fabric manager
Recall: PMAC: pod.position.port.vmid

## Slide 69: PortLand: Name Resolution (Cont.)
Edge switch intercepts ARP messages from end hosts
  To resolve IP address of destination, the edge switch needs to consult the resolver: Fabric Manager.
Send request to fabric manager, which replies with PMAC of destination host

## Slide 70: PortLand: Fabric Manager
fabric manager: logically centralized, multi-homed (ARP resolution) server
maintains topology and <IP,PMAC> mappings in “soft state”

## Slide 71: Loop-free Forwarding and Fault-Tolerant Routing
Switches build forwarding tables based on their position
  edge, aggregation and core switches
Use strict “up-down semantics” to ensure loop-free forwarding
  Load-balancing: use any ECMP path
  flow hashing to ensure packet ordering
Fault-tolerant routing:
  Mostly concerned with detecting failures
  Fabric manager maintains logical fault matrix with per-link connectivity info; inform affected switches
  Affected switches re-compute forwarding tables

## Slide 72: Outline
Data Center Introduction
Data Center Network Architectures
Fat-Tree
VL2
DCell
BCube
FiConn
Read: Sigcomm 2009 paper

## Slide 73: VL2: Motivation
  The network is a bottleneck to Data Center computation.
Today’s data center network has several issues:
  Tree architecture
    Congestion and computation hot spot
  Traffic Independence
  IP configuration Complexity
    Especially to deal with Migration
  Tradeoff
    Reliability and utilization
Read: Sigcomm 2009 paper on VL2

## Slide 74: Conventional Data Center Architecture
Notes: packet flooding and ARP broadcasts

## Slide 75: Design of VL2
Location-specific IP address(LAs)
  For all switches and interfaces or servers
Application-specific IP addresses (AAs)
  For application servers
VL2 Directory System
  Stores the mapping of AAs to LAs
  Also provides Access control
Read: VL2: A Scalable and Flexible Data Center Network, Sigcomm 2009 paper

## Slide 76: Scale-out Topologies
Aggr : Int = n:m
ToR : Aggr = 1:2

## Slide 77: Scale-out Topologies Benefit
Risk balancing
  The failure of an Int. switch reduces the bisection bandwidth by only 1/m
Routing is extremely simple on this topology
  Random path up and non-random (SPF) path down.
  Called Valiant Routing (1981) and Valiant Load Balancing
Sender S sends pkts to Dest. D via randomly chosen intermediate switch using IP-in-IP encapsulation.
AAs are from a different subnet (e.g., 20/8) and LAs from another subnet (e.g., 10/8)
Note: H(ft) denotes a hash of the five tuple

## Slide 78: Valiant load balancing
Randomization for efficient, load-balanced routing [VLB]
[VLB] Valiant Load-Balancing: Building Networks That Can Support All Traffic Matrices

## Slide 79: Example
Create by VL2 Agent
Randomly select Int. by ECMP

## Slide 80: VL2 agent
VL2 agent’s work flow
  Intercepts the ARP request for the destination Application Specific IP Address (AA)
  Converts that ARP request to a unicast query to the VL2 directory system
  Intercepts packets from the host
  Encapsulates the packet with the Location-specific IP address (LA) address obtained from the VL2 directory.
  Caches the mapping from AA to LA addresses

## Slide 81: VL2 Addressing and Routing
VL2
payload
ToR3
. . .
. . .
y
x
Servers use flat names
Switches run link-state routing and maintain only switch-level topology
y
z
payload
ToR4
z
ToR2
ToR4
ToR1
ToR3
y, z
payload
ToR3
z
. . .
Directory Service
…
x  ToR2
y  ToR3
z  ToR4
…
Lookup &
Response
…
x  ToR2
y  ToR3
z  ToR3
…
LAs
AAs
Notes: Here is how VL2 addressing and routing look like:
Switches run link-state routing and maintain only switch-level topology

## Slide 82: Random Traffic Spreading over Multiple Paths
x
y
payload
T3
y
z
payload
T5
z
IANY
IANY
IANY
IANY
Links used for up paths
Links used for down paths
T1
T2
T3
T4
T5
T6
Use a combination of ECMP and Valiant Load Balancing to distribute traffic
across intermediate paths/switches for each transfer
Notes: To overcome hot-spot-free performance for arbitrary traffic matrices, VL2 uses two related mechanisms: VLB and ECMP…goals of both are similar — VLB distributes traffic across a set of inter-mediate nodes and ECMP distributes across equal-cost paths—but each is needed to overcome limitations in the other. VL2 uses flows, rather than packets, as the basic unit of traffic spreading and thus avoids out-of-order delivery.

## Slide 83: VL2 Directory System
VL2 has a modest number (50-100 directory server nodes for 100K servers) of read-optimized, replicated directory servers that cache AA-to-LA mappings and handle queries from VL2 agents, AND
a small number (5-10 servers) of write-optimized, asynchronous replicated state machine (RSM) servers that offer a strongly consistent, reliable store of AA-to-LA mappings.
The directory servers ensure low latency, high throughput, and high availability for a high lookup rate. Meanwhile, the RSM servers ensure strong consistency and durability.

## Slide 84: VL2 Directory System
RSM
DS
RSM
DS
RSM
DS
Agent
. . .
Agent
. . .
. . .
Directory Servers
(cache)
Replicated State Machine Servers
2. Reply
2. Reply
1. Lookup
“Lookup”
5. Ack
2. Set
4. Ack
(6. Disseminate)
3. Replicate
1. Update
“Update”
strongly consistent,
reliable store of
AA-to-LA mappings
Notes: VL2 consists of (1) a modest number (50-100 servers for 100K servers) of read-optimized, replicated directory servers that cache AA-to-LA mappings and handle queries fromVL2 agents, and (2) a small number (5-10 servers) of write-optimized, asynchronous replicated state machine (RSM) servers that offer a strongly consistent, reliable store of AA-to-LA mappings. The directory servers ensure low latency, high throughput, and high availability for a high lookup rate. Meanwhile, the RSM servers ensure strong consistency and durability.

## Slide 85: Advantage of VL2
  Load Balancing
  Randomizing with VLB enables coping with Volatility
Built on well-understood networking technology
  link-state routing,
  equal-cost multi-path(ECMP) forwarding,
  IP anycasting,
  IP multicasting
Simple Migration
  Static AAs
    Only need to update AAs to LAs mapping
Eliminates the ARP and DHCP scaling bottlenecks

## Slide 86: Evaluation: testbed
80 servers
  5 for directory system
Intermediate switches (3)
  24 10Gbps Ethernet ports(3 for Aggr)
Aggregation switches(3)
  24 10Gbps Ethernet ports(3 for Aggr, 3 for ToR)
ToR (4)
  24 1Gbps ports

## Slide 87: Evaluation
Uniform high capacity:
  All-to-all data shuffle stress test:
    75 servers, deliver 500MB
    Maximal achievable goodput is 62.3
    VL2 network efficiency as 58.8/62.3 = 94%
Notes: This figure shows the aggregate goodput during a 2.7TB shuffle among 75 servers.
    We can see that the Maximal achievable goodput is 62.3, and
    VL2 network efficiency as 58.8/62.3 = 94%

## Slide 88: Critique
The extra servers are needed to support the VL2 directory system:
  Brings more cost on devices
  Hard to be implemented for data centers with tens of thousands of servers.
All links and switches are working all the time, not power efficient
No evaluation of real time performance.
Notes: But there are also some critiques:
The extra servers are needed to support the VL2 directory system,:
  Brings more cost on devices
  Hard to be implemented for data centers with tens of thousands of servers.
All links and switches are working all the times, not power efficient
No evaluation of real time performance.

## Slide 89: Outline
Data Center Introduction
Data Center Network Architectures
Fat-Tree
VL2
DCell
BCube
FiConn

## Slide 90: DCell
Existing tree structure does not scale
DCell
90
Notes: Expensive high-end switches to scale up
Single point of failure and bandwidth bottleneck
  Experiences from real systems

## Slide 91: DCell Ideas
#1: Use mini-switches to scale out
#2: Leverage servers be part of the routing infrastructure
  Servers have multiple ports and need to forward packets
#3: Use recursion to scale and build complete graph to increase capacity
Read: DCell: A Scalable and Fault-Tolerant Network Structure for Data Centers— Sigcomm 2008
Notes: The basic ideas of DCell can be summarized as follows:
#1: Use mini-switches to scale out
#2: Leverage servers be part of the routing infrastructure
  Servers have multiple ports and need to forward packets
#3: Use recursion to scale and build complete graph to increase capacity

## Slide 92: DCell: the Construction
Dcell_0
Server
Mini-switch
n servers in a DCell_0
n=2, k=0
DCell_1
n=2, k=1
Dcell_2
n=2, k=2
Build sub-DCells
Connect sub-DCells to form complete graph
End recursion by building DCell0
Notes: This slide show the Dcell architecture and the procedure to build a DCell network.

## Slide 93: BCube
Bcube
Leverage servers to be part of the routing infrastructure
  Servers have multiple ports and need to forward packets
Use recursion to scale and build complete graph to increase capacity
BCube: A High Performance, Server-centric Network Architecture for Modular Data Centers
Sigcomm 2009

## Slide 94: BCube design goals
High network capacity for various traffic patterns
  One-to-one unicast
  One-to-all and one-to-several reliable groupcast
  All-to-all data shuffling
Only use low-end, commodity switches
Graceful performance degradation
  Performance degrades gracefully as servers/switches failures increase
Notes: The design of BCube is to meet the following goals:
High network capacity for various traffic patterns
Only use low-end, commodity switches
Graceful performance degradation

## Slide 95: BCube structure
<0,0>
00
01
02
03
<0,1>
10
11
12
13
<0,2>
20
21
22
23
<0,3>
30
31
32
33
<1,0>
<1,1>
<1,2>
<1,3>
BCube0
BCube1
server
switch
Level-1
Level-0
Connecting rule
The i-th server in the j-th BCube0 connects to the j-th port of the i-th level-1 switch
shown: a BCube1 with n = 4; each server has two ports.
A BCubek network supports servers
  n is the number of servers in a BCube0
  k is the level of that BCube
A server is assigned a BCube addr (ak,ak-1,…,a0) where ai [0,k]
Neighboring server addresses differ in only one digit
Notes: This slide shows the Bcube structure.
BCube is a recursively defined structure
There are two types of devices in BCube: Servers with multiple ports, and switches that connect a constant number of servers.

## Slide 96: BCube: Server centric network
MAC addr
Bcube addr
<0,0>
00
01
02
03
<0,1>
10
11
12
13
<0,2>
20
21
22
23
<0,3>
30
31
32
33
<1,0>
<1,1>
<1,2>
<1,3>
BCube0
BCube1
MAC03
0
MAC13
1
MAC23
2
MAC33
3
port
Switch <1,3> MAC table
MAC20
0
MAC21
1
MAC22
2
MAC23
3
port
Switch <0,2> MAC table
MAC23
MAC03
20
03
data
MAC23
MAC03
20
03
data
dst
src
MAC20
MAC23
20
03
data
MAC20
MAC23
20
03
data
Server-centric BCube
  Switches never connect to other switches and only act as L2 crossbars
  Servers control routing, load balancing, fault-tolerance
MACnn are
addresses for
servers
Notes: Bcube is a server centric network.
In Bcube:
Switches never connect to other switches and only act as L2 crossbars
  Servers control routing, load balancing, fault-tolerance

## Slide 97: Multi-paths for one-to-one traffic
Theorem 1. The diameter of a BCubek is k+1
Theorem 2. There are k+1 parallel paths between any two servers in a BCubek
<0,0>
00
01
02
03
<0,1>
10
11
12
13
<0,2>
20
21
22
23
<0,3>
30
31
32
33
<1,0>
<1,1>
<1,2>
<1,3>
Notes: This slide shows the multi-paths for one-to-one traffic in Bcube.
Two parallel paths between a source server and a destina-
tion server exist if they are node-disjoint, i.e., the interme-
diate servers and switches on one path do not appear on the
other.
Two theorems hold for Bcube:
Theorem 1. The diameter of a BCubek is k+1
Theorem 2. There are k+1 parallel paths between any two servers in a BCubek
In practice, k is a small integer, typically at most 3. There-
fore, BCube is a low-diameter network.

## Slide 98: Speedup for one-to-several traffic
Theorem 3. Server A and a set of servers {di|di is A’s level-i neighbor} form an edge disjoint complete graph of diameter 2
<0,0>
00
01
02
03
<0,1>
10
11
12
13
<0,2>
20
21
22
23
<0,3>
30
31
32
33
<1,0>
<1,1>
<1,2>
<1,3>
P1
P2
P1
P2
P1
P2
Notes: Edge-disjoint complete graphs with k + 2 servers can be efficiently constructed in a Bcube of size k. These complete graphs can speed up data replications in distributed file systems like GFS.

## Slide 99: BCube Source Routing (BSR)
Server-centric source routing
  Source server decides the best path for a flow by probing a set of parallel paths
  Source server adapts to network condition by re-probing periodically or responding to failures
BSR design rationale
  Network structural property
  Scalability
  Routing performance
Notes: It is required that the routing protocol be able to fully utilize the high capacity (e.g., multi-path) of BCube and automatically load-balance the traffic.
Existing routing protocols such as OSPF and IS-IS cannot meet these requirements.
Furthermore, it is unlikely that OSPF and IS-IS can scale to several thousands of routers. As a result, Bcube uses a source routing protocol called BSR by
leveraging BCube's topological property. BSR achieves load balance and fault tolerance, and enables graceful performance degradation.

## Slide 100: BCube Source Routing
BCube stores the complete path and a next hop index (NHI) in the header of every BCube packet.
Since neighboring servers in BCube differ in only one digit in their address - reduce the space needed for an intermediate server

## Slide 101: Path compression and fast packet forwarding
<0,0>
00
01
02
03
<0,1>
10
11
12
13
<0,2>
20
21
22
23
<0,3>
30
31
32
33
<1,0>
<1,1>
<1,2>
<1,3>
Traditional address array needs 16 bytes:
Path(00,13) = {02,22,23,13}
Forwarding table of server 23
The Next Hop Index (NHI) Array needs 4 bytes:
Path(00,13)={1:2,1:2,0:3,1:1}
NHI | Output port | MAC
0:0 | 0 | Mac20
0:1 | 0 | Mac21
0:2 | 0 | Mac22
1:0 | 1 | Mac03
1:1 | 1 | Mac13
1:3 | 1 | Mac33
2 3
1 3
Fwd node
Next hop
Notes: This slide shows how path compression and fast packet forwarding is done in Bcube.
BCube stores the complete path and a next hop index (NHI) in the header of every BCube packet.

## Slide 102: Routing to external networks
Ethernet has two levels of link rates: hierarchy
  1G for end hosts and 10G for uplink
aggregator
gateway
gateway
gateway
gateway
<0,0>
00
01
02
03
<0,1>
10
11
12
13
<0,2>
20
21
22
23
<0,3>
30
31
32
33
<1,0>
<1,1>
<1,2>
<1,3>
<1,1>
10G
31
11
21
01
<1,1>
<1,3>
1G
Notes: So far, we focus on how to route packets inside a Bcube network. Now, we consider how Internal servers communicates with external computers in the Internet or other containers.
BCube uses aggregator and gateway for external communication. An aggregator is simply a commodity layer-2 switch
with 10G uplinks.

## Slide 103: Q & A